## Slide 1: Advanced-Fusion Neutron Source
National Institutes for Quantum and Radiological Science and Technology (QST) Fusion Energy Research and Development Directorate Department of Fusion Reactor Materials Research Advanced Fusion Neutron Source Design Group
Workshop on Advanced Neutron Source and its Application
4-5 November, 2017
Aomori-city, Japan
Kentaro OCHIAI

## Slide 2
Background and objectives
  Requirement from DEMO fusion reactor design
  Necessity of early neutron source
  Present status of IFMIF/EVEDA
Advanced Fusion Neutron Source
  A-FNS project based on IFMIF/EVEDA
  Site
  Basic parameters of A-FNS
  Schedule for A-FNS construction
  Issues for construction and operation
Summary
CONTENTS
1

## Slide 3
2
2015
2020
2025
2030
2035
Conceptual Design
Engineering Design
DEMO
First data acquisition
By 2035, main irradiation verification tests are required about,
・Blanket materials
Background and objectives
Candidate material validation test by fusion neutron source irradiation is an essential issue for DEMO design and it should be done by the end of engineering design phase.
We have to explore a possibility of early intense fusion neutron source construction.
・RAFM as FW
Divertor
First wall
・Diagnostic materials.
Relation of DEMO design (JA) schedule and required irradiation data for materials
・Divertor materials
Blanket
  Requirement from DEMO fusion reactor design

## Slide 4
3
Contour map of helium production rate and displacement per atom (dpa) for fusion reactor and neutron source.
DEMO reactor
The DEMO reactor will finally exposed the structure materials up to around 80 dpa.
As an initial data for the DEMO design, we think to need the irradiation up to 10 dpa/year at least.
DT neutron source including ITER is quite not sufficient from the objectives.
Fission reactor and spallation neutron sources will not be appropriate for the verification in the viewpoint of the ratio of He and dpa.
We propose the complete achievement of irradiation examination with an advanced fusion neutron source facility ,A-FNS which is like a half intensity of IFMIF by 2035.
Therefore, an fusion neutron source like a IFMIF should be operated around 2030 for the material irradiation.
  Necessity of early neutron source

## Slide 5: Present status of IFMIF/EVEDA
IFMIF Intermediate Engineering Design Report（2014）
Linear IFMIF Prototype Accelerator (ongoing)
EVEDA Lithium Test Loop (2014)
High Flux Test Module (2015)
Rokkasyo
Oarai
To achieve 9 MeV(CW) operation
Long-term stability of high speed liquid flow validated!
Prototype manufactured,
remote handling tested!
We propose an A-FNS construction using by the IFMIF/EVEDA intellectual properties.
From 2007, IFMIF/EVEDA has started to validate the construction of IFMIF on BA phase.
4

## Slide 6
Advanced Fusion Neutron Source based on IFMIF/EVEDA
Injector and RFQ+SRF
SRF and Beam transport
Test facility
Related facility
58
60
18
18
15
11
Unit: meter
Grand
Accelerator facility
From the viewpoint of the effective use, we will start to an conceptual design activity of an using by the IFMIF/EVEDA.
Cross sectional views of an A-FNS construction
Neutron point
IFMIF/EVEDA
Post Irradiation Experiment
Radio Active Processing
Target handing system
Horizontal cross sectional view of A-FNS accelerator
Advanced Fusion Neutron Source
9
5
L 160 x W 80 x H 25

## Slide 7
Basic parameters of A-FNS
40 MeV
Target
Normal
200 x 50 mm2
10-15 m/s at target
Liquid target (jet)
25 mm
Beam
200 - 270 ℃
Free surface (no window)
Neutron
6.8 x 1016 neutron/s
Deuteron
Particle
Foot print
lithium
Energy
Material
Temp.
Velocity
Thickness
Intensity
Incident angle
Current
125 mA (CW)
Window
6.0x 1014 n/cm2/s
Average flux
Helium P. R
3.12×102 appm/fpy
(at back plate)
24.7 dpa/fpy
Displacement
HePR/dpa
12.6
fpy: full power year
Schematic view of test cell (Ref. IFMIF design)
Availability
33% at least
80 mm
Neutron
Net volume for Irradiation
3cc at 25dpa/fpy
15cc at 20 dpa/fpy
30cc at 15 dpa/fpy
60cc at 10 dpa/fpy
Relation of irradiation volume and dpa/fpy (A-FNS)
High Flux Test Module

## Slide 8
110,083.72㎡
450m
245m
Construction area of A-FNS
IFERC Site
LIPAc building
The Pacific Ocean
Rokkasho, Aomori
Japan
Site of A-FNS
6

## Slide 9
2015
2020
2025
2030
2035
Conceptual Design
Engineering Design
EDA phase
Construction
Operation Phase
Pre-phase
Neutron Source for irradiation
DEMO
Construction decision
Start commissioning
First data acquisition
First irradiation
  Schedule for A-FNS construction
Conceptual design
7

## Slide 10: Issues for construction and operation
Technical feedback from the LIPAc long operation
Precise irradiation plans and their schedules
Technical issues for plant safety and regulation
Cost estimation for construction and operation
Technical issues must be solved by 2025 based on the following items.
Achievement of LIPAc
Extension of building
Extension of SRF and beam line
Safety
Safety
Purification system of Li target
Optimization of lithium target system
Remote handing for TA and TM
Remote handing from TC to PIE
Optimization of HFTM
Designs of PIE, RIP and Li-HF
As others
Storage building
Console area or building
We just start to verify the design and their development.
8

## Slide 11
Another application proposal of A-FNS
Neutron beam station of A-FNS for material analysis
RI production module installation (ex. Mo-99)
Pneumatic line to use the intense neutron field
9
A-FNS should be also utilized like multi-purposes neutron source.
( it will be available to not only for general material analysises also fusion material micro-analysis)
We just start to the investigations for the muti-purpose on A-FNS

## Slide 12
For fusion DEMO reactor design, we have started the design activity of an advanced fusion neutron source (A-FNS) facility.
From the viewpoint of the effective use of IFMIF/EVEDA intellectual properties, as a candidate, first of all, we propose the extension type .
A-FNS will be like a half size of IFMIF. The volume of irradiation will be narrow than half of IFMIF case.
A-FNS should be operated around 2030 for the data acquisition and the availability have to be 33% at least.
In case of the test facility, the hot area of remote handing will be most important issue. Especially, the exchange of Li-target assembly will be most serious action.
For the construction of A-FNS, we will need to organize a consortium, not only QST, also institutes, universities and corporations.
Summary
10

## Slide 13: Related presentations in ICFRM-18
11.6 17:00-19:00 6PT56 S.Kwon (QST, Japan) Investigation on A-FNS Neutron Spectrum Monitor System
11.7 16:40-18:40 7PT55 M. Nakamura (QST, Japan) Impact of the Beam Injection Momentum on the Free Surface of the Liquid Lithium Target of Advanced Fusion Neutron Source
11.9 16:00-18:00 9PT55 H. Kondo (QST, Japan) Experimental Study on Application of Large-Scale Cold Trap and Impurity Monitoring to Liquid Lithium for Intense Fusion Neutron Source
11.8 16:40 - 18:40 8PT56 Investigation of Mo-99 Radioisotope Production by d-Li Neutron Source M. Ohta

## Slide 15: Conceptual view of A-FNS
Horizontal cross sectional view
ECR ion injector
RFQ
SRF
MEBT
SRF
5
BD
9
40
Deuteron
Energy (MeV)
BD
14.5
26
HEBT