## Slide 1: Multi-Aimed Intense Neutron Source (MAINS) based on BISOL
Yan Sha (on behalf of BISOL-MAINS team)
State Key Laboratory of Nuclear Physics and Technology
Peking University
Workshop on Advanced Neutron Source and its Application
Nov. 04-05, 2017 Aomori, Japan

## Slide 2: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Liquid Lithium Target and Irradiation Unit
  Liquid Li Loop
  Neutron field properties
Outlook

## Slide 3: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Liquid Lithium Target and Irradiation Unit
  LLi Loop
  Neutron field properties
Outlook

## Slide 4: BISOL
Beijing Isotope-Separation-On-Line Neutron-Rich Beam Facility
— A facility to producing neutron rich rare isotope ions by means of ISOL+PF
Notes: PF: particle fragmentation

## Slide 5
Double sources
CARR (China advanced research reactor)
Intense D+ Accelerator
Notes: PF: particle fragmentation

## Slide 6: Requirements of Intense Fast Neutron Source
Basic nuclear scientific research
Material research for fusion and fission energy, neutronics, imaging, material analysis,single particle effects, ……

## Slide 7: China fusion energy roadmap
Wan, et. al., Nucl. Fusion, 57, 102009, 2017
CFETR:
5-10 dpa in Phase I
50-100 dpa in Phase II

## Slide 8: BISOL-MAINS
Multi-Aimed Intense Neutron Source driven by D+ accelerator
Isol
L-Li target
5X1014 n/cm2s
RFQ+SC Accelerator
Neutron
Lab
CARR
D+
40 MeV
10 mA
SC Accelerator
2X1014 fission/s
2X1015 fission/s
RI Ions
10 PmA
SC Accelerator
10-70 MeV/u
Isol Exp.
Exp. Term.
PF
Secondary BL
Exp. Term.
78Ni 250 pps
120Sr 2X10-4 pps
132Sr 4X1010 pps
91Kr 4X1011 pps
142Xe 9X109 pps
ECR IS
MAINS
Notes: PF: particle fragmentation

## Slide 9: MAINS
Multi-Aimed Intense Neutron Source driven by D+ accelerator
Material irradiation
(Test modules)
ISOL (Fission ion source)
Neutron science and other applications
(neutron beams)
TA
TM
TA
TA
TM
TA
TA
RIS
TA
RIS
Laser
TA
TA
TA
Irradiation Unit
Side view
Top view

## Slide 10: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Liquid Lithium Target and Irradiation Unit
  LLi Loop
  Neutron field properties
Outlook

## Slide 11: Major Milestones
2011: CIAE and PKU signed agreement to jointly promoting an ISOL-type RIB facility in Beijing area. As a result the previously proposed CARIF and ImPUF were merged into Beijing-ISOL

## Slide 12: Major Milestones
Oct. 2012: An IAC was formed and a review meeting was held at PKU to evaluate the “Initial Conceptual Design of the
BISOL”.
“The Committee considers the research potential of the proposed facility in both, basic as well as applied and interdisciplinary research, as excellent and highly competitive on the world level. It promises a unique science reach in several respects, in particular with regard to the most neutron rich exotic nuclei and the study of the astrophysical r-process.”

## Slide 13: Major Milestones
2013: the advanced ISOL-type facility was adopted in “the national mid- and long-range plan ( till 2030) of the major facilities for science and technology development”.
Aug. 2014: a Xiang Shan Forum ( 503th meeting in the series) was successfully organized and a road map for major nuclear physics research facilities was established, including the BISOL as the next major facility.
May 2016: a domestic expert meeting was held at CIAE to evaluate the preparation works of the BISOL, aiming at a proposal to the 13th 5-year plan of the central government of China.
Notes: Xiangshan meeting: national science and technology development strategy discussion.

## Slide 14: Major Milestones
May-June 2016: proposed large-scale science facilities (more than 50 proposals in all) were reviewed by the National Development and Reform Council. BISOL was successfully classed into the list of the preparation facilities (10+5 facilities in total).
Dec. 2016: the government has officially announced the results for the 13th 5-year plan.
Notes: 10 Priority +5 alternate (waiting for vacancy)

## Slide 15: Major Milestones
Jan. 2017: a specialized IAC meeting was held at PKU-CIAE, dedicated to the accelerator based intense neutron source, in particular the high-power target systems.
Mar. 2017: the 1st BISOL user meeting was held at PKU, with ～ 150 participants and very active discussions.
Jun. 2017: BISOL proposal was finalized and evaluated by an internal committee, being ready for the next national review and the next IAC review.

## Slide 16: SITE of BISOL - CIAE
Fangshan
District
Beijing
China
~11760 m2
Notes: PF: particle fragmentation

## Slide 17: SITE of BISOL - MAINS
Notes: PF: particle fragmentation

## Slide 18: Infrastructure
Notes: PF: particle fragmentation

## Slide 19: Infrastructure
Notes: PF: particle fragmentation

## Slide 20: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator preliminary design
  Liquid Lithium Target and Irradiation Unit
  LLi Loop
  Neutron field properties
Outlook

## Slide 21: MAINS
CW D+ beam: 40 MeV, 10mA (Phase I); L-Li target: 100(W)×25(T), 20 m/s
main part in -1 ~-3 layer of the BISOL building

## Slide 22: MAINS
Notes: PF: particle fragmentation

## Slide 23: MAINS
Accelerator
Irradiation facility, Li target and Li Loop

## Slide 24: BISOL-MAINS
BISOL-MAINS parameters compared to IFMIF
 | Energy (MeV) | Ion | Current (mA) | Target | Irradiation Volume (cm3) |  |  |  | 
 |  |  |  |  | >1015 n/cm2·s | >5·1014 n/cm2·s | >1014 n/cm2·s | >5·1013 n/cm2·s | >1013 n/cm2·s
BISOL-MAINS I | 40 | D+ | 10 | Liquid Li | 0 | 0 | ~12 | ~60 | ~700
BISOL-MAINS II | 40 | D+ | 20 | Liquid Li | 0 | 0 | ~60 | ~170 | ~2000
BISOL-MAINS III | 40 | D+ | 50 | Liquid Li | 0 | ~12 | ~240 | ~700 | ~7900
IFMIF | 40 | D+ | 2×125 | Liquid Li | BP | ~500 (HF) | ~6000 (MF) |  | LF

## Slide 25: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Lithium Target and Irradiation Unit
  L-Li Loop
  Neutron field properties
Outlook

## Slide 26: D+ accelerator
LEBT, RFQ, MEBT, SRF, HEBT
SRF Linac: 5 cryomodules, HWR
Total length: 75 m
Code: ParmteqM, Toutatis, TraceWin
Particles | Deuteron | 
Energy | 40 | MeV
Current | 10 | mA
Beam power | 400 | kW
rf frequency | 162.5 | MHz
Duty factor | 100 | %
Beam loss (E>3 MeV) | <1 | W/m

## Slide 27: Ion Sources
2.45 GHz, 20 mA, 50 keV H2+
2.45 GHz, 20 mA, 50 keV D+
For commissioning of accelerator instead of D+
Providing H2+ beam for experiment terminal;
As a redundancy of D+ source
PKU PMECRIS
120 mA H+
83 mA D+

## Slide 28: LEBT
2 identical solenoids whose effective pole length is 200 mm.
2 steerers (BPMs) in solenoids.
Solenoids magnetic field: 0.35T & 0.41 T, aperture 120 mm.
The total length of beam line: 1.55 m
diagnose instruments: ACCT, FC, emittance meter

## Slide 29: LEBT
ECR-IS extraction beam parameters:
RFQ entrance beam parameters:
, and mm/mrad
Match to RFQ

## Slide 30: RFQ accelerator
4 vane RFQ, quadrilateral cavity
with  mode stabilizing rods
Deposited power 96 W
RFQ kinetic parameter curves
RFQ CST model

## Slide 31: RFQ
Design strategy:
High beam transmission
Low rf power dissipation
Low surface peak field
High beam quality at the RFQ exit
Short RFQ length
Parameter | Value | Unit
Particle | D+ | 
Frequency | 162.5 | MHz
Input energy | 50 | keV
Output energy | 3.0 | MeV
Beam Current | 20 | mA
Inter-vane voltage min/max | 60/75 | kV
Vane length | 5.03 | m
Maximum peak surface electric field | 19.87 | MV/m
Kilpatrick coefficient | 1.46 | 
Minimum aperture radius | 3.05 | mm
Average aperture min/max | 3.94/5.09 | mm
Synchronous phase | -90 ~ -30 | deg
Max. modulation factor | 1.90 | 
Trans. input normalized rms emit. | 0.20 | mm·mrad
Trans. output normalized rms emit. | 0.21 | mm·mrad
Long. output rms emittance | 0.09 | MeV
Transmission ratio (PARMTEQM) (Wlimit = 0.08 MeV) | 99.41 | %
Transmission ratio (Toutatis) | 99.68 | %
Accelerator ratio (Toutatis) | 99.44 | %
Parameter | Value | Unit
Particle | D+ | 
Frequency | 162.5 | MHz
Input energy | 50 | keV
Output energy | 3.0 | MeV
Beam Current | 20 | mA
Inter-vane voltage min/max | 60/75 | kV
Vane length | 5.03 | m
Maximum peak surface electric field | 19.87 | MV/m
Kilpatrick coefficient | 1.46 | 
Minimum aperture radius | 3.05 | mm
Average aperture min/max | 3.94/5.09 | mm
Synchronous phase | -90 ~ -30 | deg
Max. modulation factor | 1.90 | 
Trans. input normalized rms emit. | 0.20 | mm·mrad
Trans. output normalized rms emit. | 0.21 | mm·mrad
Long. output rms emittance | 0.09 | 
Transmission ratio (PARMTEQM) (Wlimit = 0.08 MeV) | 99.41 | %
Transmission ratio (Toutatis) | 99.68 | %
Accelerator ratio (Toutatis) | 99.44 | %

## Slide 32: RFQ
ParmteqM multi-particle tracking with macro-particles
Envelope-X
Envelope-Y
Phase disperse
Energy disperse

## Slide 33: MEBT
3σ envelope
five gaps IH buncher
Element | Value
Cavity diameter (mm) | 370
Aperture diameter (mm) | 44
Cavity length (mm) | 320
Q value | 12000
Power (kW) | 1.9
Mode separation (MHz) | 162.3

## Slide 34: SRF linac
Beam envelop in first cryomodule
5 cryomodules, 23 SC solenoid, 32 HWR SC cavities, main coupler, and so on.
Beam loss control

## Slide 35: SRF linac
Parameters of HWR cavities
Property | Low-beta | High-beta
βopt | 0.09 | 0.15
Bore diameter [mm] | 40 | 40
Ep/Eacc | 5.3 | 4.7
Bp/Eacc [mG/(MV/m)] | 6.4 | 6.8
r/Q [Ω] | 255 | 300
Operating Eacc [MV/m] | 6 | 6
Cavity length [mm] | 271 | 350
Thickness [mm] | 3.0 | 3.0
=0.09
=0.15

## Slide 36: HEBT
Layout of HEBT
Beam 3σ envelope
Beam dump
Beam on Li target
Notes: Including 8 quadrupole, 1 octupole, 1 duodecapole

## Slide 37: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Lithium target and Irradiation Unit
  L-Li Loop
  Neutron field properties
Outlook

## Slide 38: Liquid Lithium Target
Energy and current | 40 MeV, 10 mA
Beam Power | 400 kW
Footprint | 2x(2~4) cm2
Li jet width | 10 cm
Power Density | 100 kW/cm2
Li jet thickness | 25 mm
Inlet/outlet temperature | 250/300 oC
Target Flow velocity/rate | 20 m/s, 50 L/s
Incidence angle | 5 o
Pressure in beam ducts | 10-4 Pa
Pressure in target chamber | 10-3-10-2 Pa

## Slide 39
Operation Mode I: RIS

## Slide 40: Rare Isotope Ion Source

## Slide 41
Operation Mode II: TMs

## Slide 42
Operation Mode III: Neutron Science

## Slide 43: OUTLINE
Background
Brief history of BISOL
Concept design of MAINS
  D+ Accelerator
  Lithium Target and Irradiation Unit
  L-Li Loop
  Neutron field properties
Outlook

## Slide 44: Li Loop
 | Main loop | Secondary loop | Third loop | Impurity loop |  | 
 |  |  |  | Cold trap | Heat trap 1 | Heat trap 2
Working Substance | L-Li | oil | oil | Ar | Ti | Y
Temperature(℃) | 250 | 185-220 | 50-75 | 200 | 600 | 280-300
Pressure (bar) | 4 | 5 | 5 |  |  | 
Max Flux (l/s) | 65 | 85 | 130 |  |  | 

## Slide 45: Access Cell
Notes: PF: particle fragmentation

## Slide 46: Access route
Taking out TA/TMs/RIS from TC
Waiting for cooling (short life Isotopes)
Disassembling TA/TMs/RIS (radioactive waste directly down)
Component handling
Rig handling
To PIE
Magnet maintenance
New components
Finished new TA/TMs/RIS
Replacing TA/TMs/RIS into TC
Magnet maintenance












## Slide 47: OUTLINE
Background
Brief history of BISOL
Concept of MAINS
  D+ Accelerator
  Li target and Irradiation Unit
  L-Li Loop
  Neutron field properties
Outlook

## Slide 48: Neutron flux density distribution
n flux: > 1014 n/cm2s > 5X1013 n/cm2s > 1013 n/cm2s
dpa in steel > 8 dpa/fpy > 4.4 dpa/fpy > 1.3 dpa/fpy
Volume: ~ 12 cm3 ~ 60 cm3 ~ 700 cm3
Phase I
40 MeV 10 mA
D+Li

## Slide 49: BISOL-MAINS
The neutron flux density distribution at the Test Module position (2 mm beyond BP)
The maximum neutron flux density reaches 2X1014 cm-2s-1 on test module
Li target and the test module

## Slide 50: Neutron Energy
0°Neutron energy spectrum
BISOL-MAINS @10 mA D+
IFMIF and SPIRA II

## Slide 51: OUTLINE
Background
Brief history of BISOL
MAINS concept D+ Accelerator
  Lithium Target and Irradiation Unit
  L-Li Loop
  Transportation and Waste Treatment
Outlook

## Slide 52: Time Schedule for BISOL-MAINS
Year | 2018 |  | 2020 |  | 2022 |  | 2024 |  | 2026 |  | 2028 |  | 2030 |  | 203？ | 
Re-evaluation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Concept & Engineering Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation @ 5-10 mA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commissioning & Operation @ 20 mA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
From 20 mA to 50 mA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 53: Oct. 2015 ELTL running 1560 h
Accumulated operation time of EVEDA Lithium Test Loop (ELTL) of the lithium target reached 1,560 h.
Notes: Including 8 quadrupole, 1 octagon, 1 dodecahedron

## Slide 54: June 5, 2017 25MeV 150-200 μA CW P Beam!
CiADS 25 MeV proton linac past CW proton beam with 150-200 μA CW current and >10 mA peak current (IMP and IHEP)
Notes: Including 8 quadrupole, 1 octagon, 1 dodecahedron

## Slide 55: Appreciation
We appreciate all helps and support from domestic and international experts and colleagues.
We need more communication, and cooperation with IFMIF-like neutron source partners.

## Slide 56: Thanks for attention!